Draft Plan

P-3 ARCTAS Test Flight #1

25 Mar 2008

Assumes cloud conditions above Chesapeake Lighthouse are acceptable (little or no cirrus, little or no mid-level cloud, and no or uniform low cloud).

Takeoff: 11:00 local

Waypoints:

2: Chesapeake Lighthouse (COVE)

3: Yorktown Power Plant (alternate: Chesapeake Power Plant)

| Point | 1 | 2 | 3 | 4 |
| --- | --- | --- | --- | --- |
| Latitude | 37.93306 | 36.90463 | 37.22 | 37.93306 |
| Longitude | -75.4722 | -75.7127 | -76.51 | -75.4722 |
| Cum. Flt. Time | 0:00 | 0:12 | 2:10 | 2:32 |
| Leg Flt. Time |  | 0:12 | 0:08 | 0:12 |
| Local Time | 11:00 | 11:12 | 13:10 | 13:32 |
| UTC | 15:00 | 15:12 | 17:10 | 17:32 |
| Delay |  | 1:50 | 0:10 |  |
| Leg Speed (m/s) | 160 | 160 | 160 | 160 |
| Leg Speed (kt) | 311 | 311 | 311 | 311 |
| UTC diff: | 4 |  |  |  |

Profile data:

|  | Cumulative Time |  |  |  |
| --- | --- | --- | --- | --- |
| Duration | Minutes | hh:mm | Altitude, kft | Flight Level, 100s of ft | Notes |
| 0 | 0 | 0:00 | 0 | 0 |  |
| 12 | 12 | 0:12 | 12 | 120 | Climb ~1,000 fpm to COVE |
| 20 | 32 | 0:32 | 12 | 120 | Leak tests & SSFR triangle above COVE |
| 12 | 44 | 0:44 | 0.2 | 2 | Spiral down to 200 ft or cloud top |
| 10 | 54 | 0:54 | 0.2 | 2 | Straight & level leg past COVE |
| 1 | 55 | 0:55 | 0.6 | 6 |  |
| 10 | 65 | 1:05 | 0.6 | 6 | CAR circles at COVE |
| 2 | 67 | 1:07 | 2 | 20 |  |
| 10 | 77 | 1:17 | 2 | 20 | CAR circles at COVE |
| 5 | 82 | 1:22 | 6 | 60 |  |
| 10 | 92 | 1:32 | 6 | 60 | CAR circles at COVE |
| 4 | 96 | 1:36 | 6 | 60 | Staight & level |
| 6 | 102 | 1:42 | 6 | 60 | 2 AATS test circles at COVE |
| 4 | 106 | 1:46 | 6 | 60 | Staight & level |
| 6 | 112 | 1:52 | 6 | 60 | 2 AATS test circles at COVE |
| 10 | 122 | 2:02 | 6 | 60 | Straight & level leg past COVE |
| 8 | 130 | 2:10 | 1 | 10 | Head for power plant plume |
| 10 | 140 | 2:20 | 1 | 10 | Work to sample plume |
| 12 | 152 | 2:32 | 0 | 0 | Return to base |

Track thru W72 37’, N37 15’ is Terra Track 19, 25 Mar 2008, 15:45:30 UT, SZA 38.282.