## Slide 1
Lessons Learned:
Ground power on aircraft at WFF
With reliable KU, Real-Time dual regression retrievals served in MTS with 40 to 45s second latency
S-HIS: Operated Nominally with NO Downtime
Engineering and Radiance data example

## Slide 2
Real-Time Dual Regression (DR) Retrievals
Real-Time DR: 40 to 45s second latency, frequency
DRSH transit time from aircraft to ground, <0.7s
transit time WFF to CA to WI, ~0.2s
RDR to SDR (calibration) processing time, ~0.3s
RT-DR EDR (retrieval) runs every ~35s on latest data, ~35s
KML generation, ~0.2s?
minimum refresh of MTS, 10s

## Slide 3
Real-Time Dual Regression (DR) Retrievals
x-sections of individual footprint retrievals
Skew-t of mean retrieval
10 minute history of CTP

## Slide 4
15-Sep-2012, S-HIS RH cross-sections
15-Sept
DR CTP versus CTT
UWPHYSRET
AVAPS
Dual Regression (DR)
UWPHYSRET
07-Sept
Clear Sky Comparison
T, RH, and cloud retrieval characterization (work in progress)
RH over ice
RH over water