## Slide 1: High-Altitude Imaging Wind and Rain Airborne Profiler (HIWRAP) Status
Stephen Guimond U. MD/ESSIC
Lin Tian Morgan State Univ.
James Carswell Remote Sensing Solutions
Gerry Heymsfield NASA/Goddard Space Flight Center
Lihua Li, Matt Mclinden, NASA/Goddard Space Flight Center
Michael Coon, M. Perrine,
Amber Reynolds
HAMSR
HIWRAP
HIRAD
Picture of AV-1 Aircraft at Edwards AFB

## Slide 2: High-Altitude Imaging Wind and Rain Airborne Profiler (HIWRAP)
New technologies in HIWRAP: Solid-state transmitters with novel frequency diversity pulse compression waveforms & Ku/Ka-band single aperture antenna.
Parameters | Specifications | 
 | Ku-band | Ka-band
Inner/Outer Frequency (GHz) | 13.91,13.47 | 35.56, 33.72
Peak Transmit Power (W) | 25 | 4
3 dB Beamwidth (o) | 2.9 | 1.2
Polarization | H (inner beam), V (outer beam) | 
Dynamic Range (dB) | > 65 | 
Min. Detect. Reflectivity (dBZe ,60m,10 km range) | 0 | -5
Doppler Velocity (ms-1) | 0-150 (< 1.5 ms-1 @ SNR > 10) | 
Conical Scanning | 10-30 RPM (nom. 16 RPM) | 
MEASUREMENTS GOALS:
Precipitation and 3-D winds
Ocean surface vector winds in clear to light rain regions
30 km
Notes: GPM frequencies
Combine volume scattering signal and surface scattering

## Slide 3
HIWRAP Pulse Sequence
 | OP1 | OC | OP2 | IP1 | IC | IP2
Ku | 122 | 112 | 130 | 126 | 116 | 134
Ka | 115 | 108 | 122 | 118 | 111 | 125
IF Frequencies (MHz)
Short pulse 1 is for near-surface measurement (2 msec )
Chirp is for higher resolution/sensitivity (20 msec )
Short pulse 2 is for ranges close to radar (2 msec )
Pulse Repetition Time 1 (PRT)
Pulse Repetition Time 2 (PRT)
Dual PRF for unfolding
8-frequencies
~4000 Hz
~5000 Hz
Notes: Move me

## Slide 4: Polar Plot: 17 Sept 2010 Hurricane Karl
Reflectivity Doppler (air+fall speed)
HIWRAP: 20 crossings of Hurricane Karl on Sept. 17, 2010 during GRIP over 14 hours.
Doppler line of sight wind measurements are continually profiled during the conical scans.
Ku-band 30o H
Ku-band 30o H
Measurement Geometry

## Slide 5: HS3 5-6 Nov 2012 Flight
Flight over the Pacific with emphasis on obtaining ocean surface winds.
Develop/evaluate HIRAD ocean wind retrievals.
HIWRAP obtained the first real-time data plots during AV-1 flights.
HIWRAP performance improved over GRIP.
<- First real-time data collected.
vert
2 km
4 km

## Slide 6: Reflectivity 5-6 Nov 2012
Outer, Inner Beam. Ku- and Ka-Band..
-> Ka higher sensitivity and resolution.
Frontal System off Oregon Coast

## Slide 7: HIWRAP Doppler Unfolding
Automated “Dual-PRF” unfolding followed by a second unfold based on aircraft Doppler component.
Working through details to make this more reliable.
Ka-band is more problematic because of low Nyquist velocity
Future: frequency diversity unfolding: Testing 2013.
Aircraft motion
Ku
folded
Ka
folded
PRF: 4000, 5000 Hz
Pulse-pair velocities: low PRF, high PRF, dual PRF
Ku: 20, 25, 100 m/s
Ka: 8, 10, 40 m/s

## Slide 8: Pulse Compression – Range Side-lobes
Comparison between Linear and Non-linear frequency modulation (NLFM)
Surface sidelobes
Nonlinear FM Tapered Waveforms (2013)
Linear FM Un-tapered Waveforms
Prior to 2013 flights
Amplitude tapering improves channel isolation
Frequency
Frequency
Time
Time
Extreme Case with nadir pointing HIWRAP

## Slide 9: HIWRAP Data Flow
Raw I, Q
8 sub channels
2-freq, 2-beams, chirp, pulse (~6 TB/flight)
Navigation
Antenna Rotation Angle
Radar Status
Merged File
Unfolding
Pulse Compression Filter & Pulse Pair
Data Merge
Calibration
Chirp & pulse merge*
Stored on plane
Post Processed
netCDF file
Disk File
Data System

## Slide 10: Wind Retrieval Algorithms (Atmosphere)
  Grid point analysis -> 3D winds
    Guimond et al. Poster at meeting.
  VAD analysis -> 2D plane at nadir with linear assumption.
    Tian et al. Poster at meeting.
  “Coplane” 3D analysis (Didlake) experimental
  Good progress on wind algorithms and wind error analysis -> testing hampered by noisy GRIP data and unfolding issues.

## Slide 11
~ 3 km height Ku-band Reflectivity (dBZ) & Wind Vectors
Grid-point Analysis of Hurricane Karl (2010) Intensification During GRIP
Grid-point analysis using inner (30 degree) beam.
Notes: These are North to South GH overpasses of Hurricane Karl from HIWRAP. The passes span a total of ~ 12 hours with roughly 2 hrs between each N-S pass.
Actual delta T between each pass is: 2.25 h, 2.2 h, 2.5 h, 3 h, 1.67 h

## Slide 12
Nadir Wind retrieval for HIWRAP
Vertical particle velocity (m/s)
Cross-track wind, VAD, (m/s)
Reflectivity (dBZ), Ku, inner, fore
Doppler, Ku, inner, fore
Along-track wind, DD, (m/s)
Along-track wind, VAD, (m/s)
Along –track wind from dual-Doppler and VAD analyses agree in general;
Vertical wind from dual-Doppler analysis is used to compute the divergence assuming linear wind field in each VAD scan.

## Slide 13: Ocean Winds
6 Nov 2013Flight
Along-track pixels
Calib. NRCS at 40o incidence angle bounded by 7 and 10 m/s NSCAT2 Geophys. Model Function
Wind direction
214o
10 m/s
7 m/s
Wind Direction vs Scan Number
Wind Speed vs Scan Number
NRCS vs Scan Number
One scan
Calibration Stage
40 scans
0
10
180
240

## Slide 14
Planned HIWRAP Upgrades for
2013 HS3 Flights
Ka-band transceiver upgrade ~10 dBZ sensitivity improvement.
  Upgrade from ~6 Watt to 50 Watt peak power
  Improved receiver noise floor.
IF subsystem upgrade/replacement resulting in improved channel-channel isolation.

## Slide 15
Pulse compression improvement with NLFM.
  New FPGA-based waveform generator capable of non-linear waveforms with amplitude tapering.
  Expected range sidelobe reduction of 7+ dB.
Onboard Pulse Pair and Pulse Compression processing.
  Reduction of data volume.
  Enabling tech for real-time Doppler data.
  Improved data disk reliability.
Outstanding Issues:
  GPS battery control
  GPS interference from Irridium?.
  Thermal issues with solid state disks.
Planned HIWRAP Upgrades for
2013 HS3 Flights

## Slide 16
  Planned 2013
    Real-time uncalibrated reflectivity plots available in the control room for scientist use.
    (Experimental) Real-time Doppler velocities corrected for aircraft motion made available for possible real-time wind vector estimates.
    Reflectivity will be available in two horizontal slices and a vertical curtain below the aircraft.
  Future Possibilities
    Low resolution wind products (gridded, VAD, ..)
    Doppler data for assimilation
    Ocean surface wind vector
Real-Time Data Plans

## Slide 17: HAR Web Site http://har.gsfc.nasa.gov

## Slide 18: Questions?